## Slide 1
RIS-based antenna: Antenna performance
RIS-based antenna
  RIS + feed (horn antenna)
  Capable of beam sweeping, just like the phased array
  More energy and cost efficient than conventional phased array
Performance indicator
  Sidelobe level: difference between the strongest sidelobe and the main lobe
  Beam steering precision: the deviation of the main lobe from the desired direction
Sidelobe level

## Slide 2
RIS-based antenna: Antenna performance
Implemented RIS-based antenna
  RIS: 32*32 elements, 1bit, 25~27GHz
  Feed: horn antenna LB-34-10-C-KF, 10 dBi
RIS
Feed

## Slide 3
RIS-based antenna: Antenna performance
Experimental setup
  Test the antenna within an anechoic chamber in order to measure the performance metrics accurately
Turn table for supporting RIS-based antenna
Spherical-to-plane wave transformation plate

## Slide 4
RIS-based antenna: Antenna performance
Experimental results
  Sidelobe level
  Beam steering precision
Beam direction (degree) | -10 | 0 | 10
SLL (dB) | -14.5 | -14.2 | -12.2
Target Beam direction (degree) | -10 | 0 | 10
Deviation (degree) | 0.66 | 0 | 1.08