## Slide 1
Principle
  The RIS-based antenna radiates out two EM waves with orthogonal polarizations towards two users , and each EM wave carries one data stream
Performance indicator and requirement
  EVM: for 64QAM modulation
  ACLR: <-30 dBc
Communication Prototype
RIS-based antenna: Dual stream transmission performance
  One transmitter+ two receivers
  Transmitter
    Utilize two signal generators to output two data streams
    The two data streams are radiated out through two linearly polarized RIS-based antennas, respectively.

## Slide 2
Experimental setup
  In a meeting room
  Reflection angles for two receivers: and
  Tx-Rx distances: 4m
RIS-based antenna: Dual stream transmission performance
RIS 2
Feed 1
Rx antenna 2
Tx antenna
Rx antenna 1
RIS 1
Feed 2

## Slide 3
Experimental results
RIS-based antenna: Dual stream transmission performance
ACLR=-33.59 dBc
EVM=3.04%
Rx 1

## Slide 4
Experimental results
RIS-based antenna: Dual stream transmission performance
ACLR=-29.66 dBc
EVM=3.80%
Rx 2
Conclusion: the RIS-based antenna can support dual stream communication with satisfying EVM and ACLR