## Slide 1
RIS-based antenna: Single stream transmission performance
Performance indicator and requirement
  Error Vector Magnitude (EVM)
    Definition
      Error vector: a vector in the I-Q plane between the ideal constellation point and the received point
      EVM: root mean square of error square normalized by ideal signal amplitude
    Physical meaning: EVM measures how far the received symbols are from the ideal constellations.
    Requirement: different requirements under various modulation modes
EVM requirement

## Slide 2
RIS-based antenna: Single stream transmission performance
Performance indicator and requirement
  Adjacent Channel Leakage Ratio (ACLR)
    Definition: ratio between the power within the designated channel and the power within adjacent channels
    Physical meaning: a measurement of the interference to adjacent channels
    Requirement: <-30dBc

## Slide 3
Communication Prototype
  One Transmitter
    Vector signal generator (SMW200A): generate signal
    One RIS-based antenna
  One Receiver:
    Horn antenna
    Lower noise amplifier (30dB)
    Spectrum analyzer (FSW): measure ACLR and EVM
RIS-based antenna: Single stream transmission performance
Vector signal generator
Spectrum analyzer

## Slide 4
Experimental setup
  In a meeting room
  Transmit power: 1 dBm
  Transmit bandwidth: 400MHz
  Adjacent channel bandwidth: 400MHz for each side
RIS-based antenna: Single stream transmission performance
RIS
Feed
Rx antenna
Reflection angle
Tx antenna

## Slide 5
Experimental results
  EVM (Reflection angle=)
  ACLR (Tx-Rx distance=4m)
  Conclusion: RIS-based antenna can support single stream communication with required ACLR and EVM under a wide range of Tx-Rx distances and reflection angles.
Tx-Rx distance (m) | 4 | 8 | 12 | 16 | 20
EVM (%) | 2.9 | 3.42 | 4.26 | 4.39 | 4.8
Reflection angle (degree) | 0 | 30 | 60
ACLR (dBc) | -33.36 | -35.51 | -30.44
Table II. ACLR vs. reflection angle, with center frequency=25.2GHz
Reflection angle (degree) | 0 | 30 | 60
ACLR (dBc) | -30.05 | -31.0 | -30.1
Table III. ACLR vs. reflection angle, with center frequency=26.8GHz
RIS-based antenna: Single stream transmission performance